## Slide 1: INST 346 Spring 2025
Lecture 19
April 7, 2025
Professor Keith Marzullo

## Slide 2: Network layer data plane: Learning objectives
Overview of network layer: data versus control plane
What’s inside a router
IP: the Internet Protocol
Generalized forwarding, SDN
Middleboxes

## Slide 3: What’s inside a router

## Slide 4: Router architecture overview
high-level view of generic router architecture:
high-speed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware) operates in nanosecond timeframe
routing, management
control plane (software)
operates in millisecond
time frame

## Slide 5: Input port functions: 1
switch
fabric
line
termination
physical layer:
bit-level reception
link
layer
protocol
(receive)
link layer:
e.g., Ethernet
(chapter 6)
Frame
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
input port queuing: if datagrams arrive faster than forwarding rate into switch fabric
Datagram
Notes: Green box is a physical layer responsible for receiving bit level transmission. Copper, fiber wireless.
Link layer in blue – bit assemble into Ethernet frame. We will discuss this in details in chapter 6.
But most critical one, is here. Lookup, forwarding function. Lookup and forward is “Match plus action” behavior.
GOAL – processing at “line speed”, otherwise, buffer will be full and packet will be lost

## Slide 6: Input port functions: 2
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
destination-based forwarding: forward based only on destination IP address (traditional)
generalized forwarding: forward based on any set of header field values
line
termination
lookup,
forwarding
queueing
physical layer:
bit-level reception
switch
fabric
link
layer
protocol
(receive)
link layer:
e.g., Ethernet
(chapter 6)

## Slide 7: Destination-based forwarding: 1
Q: What happens if ranges don’t divide up so nicely?
200.23.16.0
through
200.23.23.255
200.23.24.0
through
200.23.24.255
200.23.25.0
through
200.23.25.255
Notes: Text for this animation:
This all works out pretty nice and looks pretty simple!
But of course the devil is in the details, as the saying goes.
What happens, for example, when a subset of addresses say in this first range should go to say interface 3, rather than interface 0. Well, of course we could split the first address range into multiple pieces, and add in this new subrange with its new destination output port. But it turns out there’s a much simpler and elegant way to do this. Known as longest prefix matching.

## Slide 8: Destination-based forwarding: 2
3
Notes: Text for this animation:
This all works out pretty nice and looks pretty simple!
But of course the devil is in the details, as the saying goes.
What happens, for example, when a subset of addresses say in this first range should go to say interface 3, rather than interface 0. Well, of course we could split the first address range into multiple pieces, and add in this new subrange with its new destination output port. But it turns out there’s a much simpler and elegant way to do this. Known as longest prefix matching.

## Slide 9: Longest prefix matching: 1
when looking for the forwarding table entry for a given destination address, use longest address prefix that matches destination address.
longest prefix match

## Slide 10: Longest prefix matching: 2
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
********
***
********
***
********

## Slide 11: Longest prefix matching: 3
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
********
***
********
***
********
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
11001000 00010111 00010110 10100001

## Slide 12: Longest prefix matching: 4
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 13: Longest prefix matching: 5
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 14: Longest prefix matching: 6
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 15: Longest prefix matching: 7
we’ll see why longest prefix matching is used shortly, when we study addressing
longest prefix matching: often performed using ternary content addressable memories (TCAMs)
  content addressable: present address to TCAM: retrieve address in one clock cycle, regardless of table size
  Cisco Catalyst: ~1M routing table entries in TCAM

## Slide 16: Switching fabrics: 1
transfer packet from input link to appropriate output link
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
high-speed
switching
fabric
N input ports
N output ports
. . .
. . .
R
R
R
R
(rate: NxR, ideally)

## Slide 17: Switching fabrics: 2
bus
memory
memory
interconnection
network
three major types of switching fabrics:
transfer packet from input link to appropriate output link
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable

## Slide 18: Sidebar: Network Neutrality: 1
What is network neutrality?

## Slide 19: Sidebar: Network Neutrality: 2
What is network neutrality?
  technical: how an ISP should share/allocation its resources
  packet scheduling, buffer management are the mechanisms

## Slide 20: Sidebar: Network Neutrality: 3
What is network neutrality?
  technical: how an ISP should share/allocation its resources
  packet scheduling, buffer management are the mechanisms
  social, economic principles
    protecting free speech
    encouraging innovation, competition

## Slide 21: Sidebar: Network Neutrality: 4
What is network neutrality?
  technical: how an ISP should share/allocation its resources
  packet scheduling, buffer management are the mechanisms
  social, economic principles
    protecting free speech
    encouraging innovation, competition
  enforced legal rules and policies
Different countries have different “takes” on network neutrality

## Slide 22: Sidebar: Network Neutrality: 5
2015 US FCC Order on Protecting and Promoting an Open Internet: three “clear, bright line” rules:

## Slide 23: Sidebar: Network Neutrality: 6
2015 US FCC Order on Protecting and Promoting an Open Internet: three “clear, bright line” rules:
no blocking … “shall not block lawful content, applications, services, or non-harmful devices, subject to reasonable network management.”

## Slide 24: Sidebar: Network Neutrality: 7
2015 US FCC Order on Protecting and Promoting an Open Internet: three “clear, bright line” rules:
no blocking … “shall not block lawful content, applications, services, or non-harmful devices, subject to reasonable network management.”
no throttling … “shall not impair or degrade lawful Internet traffic on the basis of Internet content, application, or service, or use of a non-harmful device, subject to reasonable network management.”

## Slide 25: Sidebar: Network Neutrality: 8
2015 US FCC Order on Protecting and Promoting an Open Internet: three “clear, bright line” rules:
no blocking … “shall not block lawful content, applications, services, or non-harmful devices, subject to reasonable network management.”
no throttling … “shall not impair or degrade lawful Internet traffic on the basis of Internet content, application, or service, or use of a non-harmful device, subject to reasonable network management.”
no paid prioritization. … “shall not engage in paid prioritization”

## Slide 26: ISP: telecommunications or information service? 1
Is an ISP a “telecommunications service” or an “information service” provider?
the answer really matters from a regulatory standpoint!

## Slide 27: ISP: telecommunications or information service? 2
US Telecommunication Act of 1934 and 1996:
  Title II: imposes “common carrier duties” on telecommunications services: reasonable rates, non-discrimination and requires regulation
  Title I: applies to information services:
    no common carrier duties (not regulated)
    but grants FCC authority “… as may be necessary in the execution of its functions”4
Is an ISP a “telecommunications service” or an “information service” provider?
the answer really matters from a regulatory standpoint!

## Slide 28: Network Layer: Internet: 1
host, router network layer functions:
transport layer: TCP, UDP
link layer
physical layer
network
layer

## Slide 29: Network Layer: Internet: 2
host, router network layer functions:
transport layer: TCP, UDP
link layer
physical layer
network
layer
forwarding
table
Path-selection algorithms: implemented in
routing protocols (OSPF, BGP)
SDN controller

## Slide 30: Network Layer: Internet: 3
host, router network layer functions:
transport layer: TCP, UDP
link layer
physical layer
network
layer
forwarding
table
Path-selection algorithms: implemented in
routing protocols (OSPF, BGP)
SDN controller
IP protocol
datagram format
addressing
packet handling conventions

## Slide 31: Network Layer: Internet: 4
host, router network layer functions:
IP protocol
datagram format
addressing
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer
forwarding
table
Path-selection algorithms: implemented in
routing protocols (OSPF, BGP)
SDN controller

## Slide 32: IP Datagram format: 1
32-bit destination IP address
ver
length
32 bits
payload data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
destination IP address
options (if any)
IP protocol version number
header length(bytes)
total datagram
length (bytes)
Maximum length: 64K bytes
Typically: 1500 bytes or less

## Slide 33: IP Datagram format: 2
ver
length
32 bits
payload data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
destination IP address
options (if any)
upper layer protocol (e.g., TCP or UDP)
“type” of service:
diffserv (0:5)
ECN (6:7)
TTL: remaining max hops
(decremented at each router)

## Slide 34: IP Datagram format: 3
ver
length
32 bits
payload data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
destination IP address
options (if any)
fragmentation/
reassembly
header checksum

## Slide 35: IP Datagram format: 4
ver
length
32 bits
payload data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
destination IP address
options (if any)
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead for TCP+IP
overhead
e.g., timestamp, record route taken
32-bit source IP address
32-bit destination IP address

## Slide 36: IP addressing: introduction 1
IP address: 32-bit identifier associated with each host or router interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27

## Slide 37: IP addressing: introduction 2
IP address: 32-bit identifier associated with each host or router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27

## Slide 38: IP addressing: introduction 3
IP address: 32-bit identifier associated with each host or router interface
interface: connection between host/router and physical link
  routers typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
dotted-decimal IP address notation:

## Slide 39: IP addressing: introduction 4
Q: how are interfaces actually connected?
For now: don’t need to worry about how one interface is connected to another (with no intervening router)
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A: wired
Ethernet interfaces connected by Ethernet switches
A: wireless WiFi interfaces connected by WiFi base station
A: we’ll learn about that in chapters 6, 7

## Slide 40: Subnets: 1
What’s a subnet ?
  device interfaces that can physically reach each other without passing through an intervening router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
network consisting of 3 subnets

## Slide 41: Subnets: 2
What’s a subnet ?
  device interfaces that can physically reach each other without passing through an intervening router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
network consisting of 3 subnets
IP addresses have structure:
  subnet part: devices in same subnet have common high order bits
  host part: remaining low order bits

## Slide 42: Subnets: 3
Recipe for defining subnets:
detach each interface from its host or router, creating “islands” of isolated networks
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27

## Slide 43: Subnets: 4
Recipe for defining subnets:
detach each interface from its host or router, creating “islands” of isolated networks
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27

## Slide 44: Subnets: 5
Recipe for defining subnets:
detach each interface from its host or router, creating “islands” of isolated networks
each isolated network is called a subnet
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27

## Slide 45: Subnets: 6
Recipe for defining subnets:
detach each interface from its host or router, creating “islands” of isolated networks
each isolated network is called a subnet
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
subnet mask: /24
(high-order 24 bits: subnet part of IP address)
subnet
223.1.3.0/24
subnet 223.1.1.0/24
subnet 223.1.2.0/24

## Slide 46: Subnets: 7
where are the subnets?
what are the /24 subnet addresses?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
223.1.2.1

## Slide 47: Subnets: 8
where are the subnets?
what are the /24 subnet addresses?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
223.1.2.1

## Slide 48: Subnets: 9
where are the subnets?
what are the /24 subnet addresses?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
223.1.2.1
subnet 223.1.2/24
subnet 223.1.9/24
subnet 223.1.1/24
subnet 223.1.7/24
subnet 223.1.3/24
subnet 223.1.8/24

## Slide 49: IP addressing: CIDR
CIDR: Classless InterDomain Routing (pronounced “cider”)
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23

## Slide 50: IP addresses: how to get one? 1
That’s actually two questions:
Q: How does a host get IP address within its network (host part of address)?
Q: How does a network get IP address for itself (network part of address)

## Slide 51: IP addresses: how to get one? 2
That’s actually two questions:
Q: How does a host get IP address within its network (host part of address)?
Q: How does a network get IP address for itself (network part of address)
How does host get IP address?
hard-coded by sysadmin in config file (e.g., /etc/rc.config in UNIX)
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”

## Slide 52: DHCP: Dynamic Host Configuration Protocol 1
goal: host dynamically obtains IP address from network server when it “joins” network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/on)
  support for mobile users who join/leave network

## Slide 53: DHCP: Dynamic Host Configuration Protocol 2
goal: host dynamically obtains IP address from network server when it “joins” network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/on)
  support for mobile users who join/leave network
DHCP overview:
  host broadcasts DHCP discover msg [optional]
  DHCP server responds with DHCP offer msg [optional]
  host requests IP address: DHCP request msg
  DHCP server sends address: DHCP ack msg

## Slide 54: DHCP client-server scenario: 1
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
DHCP server
223.1.2.5
arriving DHCP client needs
address in this network
Typically, DHCP server will be co-located in router, serving all subnets to which router is attached

## Slide 55: DHCP client-server scenario: 2
DHCP server: 223.1.2.5
Arriving client
Broadcast: is there a DHCP server out there?

## Slide 56: DHCP client-server scenario: 3
DHCP server: 223.1.2.5
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654

## Slide 57: DHCP client-server scenario: 4
DHCP server: 223.1.2.5
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
Broadcast: I’m a DHCP server! Here’s an IP address you can use
DHCP offer

## Slide 58: DHCP client-server scenario: 5
DHCP server: 223.1.2.5
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs

## Slide 59: DHCP client-server scenario: 6
DHCP server: 223.1.2.5
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
The two steps above can be skipped “if a client remembers and wishes to reuse a previously allocated network address” [RFC 2131]

## Slide 60: DHCP client-server scenario: 7
DHCP server: 223.1.2.5
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
The two steps above can be skipped “if a client remembers and wishes to reuse a previously allocated network address” [RFC 2131]
DHCP request
Broadcast: OK. I would like to use this IP address!

## Slide 61: DHCP client-server scenario: 8
DHCP server: 223.1.2.5
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
The two steps above can be skipped “if a client remembers and wishes to reuse a previously allocated network address” [RFC 2131]
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs

## Slide 62: DHCP client-server scenario: 9
DHCP server: 223.1.2.5
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
The two steps above can be skipped “if a client remembers and wishes to reuse a previously allocated network address” [RFC 2131]
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: OK. You’ve got that IP address!

## Slide 63: DHCP client-server scenario: 10
DHCP server: 223.1.2.5
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
The two steps above can be skipped “if a client remembers and wishes to reuse a previously allocated network address” [RFC 2131]
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs

## Slide 64: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client (“default gateway”)
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 65: DHCP: example 1
Connecting laptop will use DHCP to get IP address, address of first-hop router, address of DNS server.
router with DHCP
server built into
router
168.1.1.1

## Slide 66: DHCP: example 2
Connecting laptop will use DHCP to get IP address, address of first-hop router, address of DNS server.
router with DHCP
server built into
router
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP REQUEST message encapsulated in UDP, encapsulated in IP, encapsulated in Ethernet

## Slide 67: DHCP: example 3
Connecting laptop will use DHCP to get IP address, address of first-hop router, address of DNS server.
router with DHCP
server built into
router
168.1.1.1
DHCP
DHCP REQUEST message encapsulated in UDP, encapsulated in IP, encapsulated in Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server

## Slide 68: DHCP: example 4
Connecting laptop will use DHCP to get IP address, address of first-hop router, address of DNS server.
router with DHCP
server built into
router
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP REQUEST message encapsulated in UDP, encapsulated in IP, encapsulated in Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet de-mux’ed to IP de-mux’ed, UDP de-mux’ed to DHCP

## Slide 69: DHCP: example 5
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
router with DHCP
server built into
router
DHCP
UDP
IP
Eth
Phy
DHCP

## Slide 70: DHCP: example 6
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulated DHCP server reply forwarded to client, de-muxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP

## Slide 71: DHCP: example 7
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulated DHCP server reply forwarded to client, de-muxing up to DHCP at client
client now knows its IP address, name and IP address of DNS server, IP address of its first-hop router
router with DHCP
server built into
router
DHCP

## Slide 72: IP addresses: how to get one? 3
Q: how does network get subnet part of IP address?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20

## Slide 73: IP addresses: how to get one? 4
Q: how does network get subnet part of IP address?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
ISP can then allocate out its address space in (say) 8 blocks:
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 74: IP addressing: last words ... 1
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned Names and Numbers http://www.icann.org/
  allocates IP addresses, through 5 regional registries (RRs) (who may then allocate to local registries)
  manages DNS root zone, including delegation of individual TLD (.com, .edu , …) management

## Slide 75: IP addressing: last words ... 2
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned Names and Numbers http://www.icann.org/
  allocates IP addresses, through 5 regional registries (RRs) (who may then allocate to local registries)
  manages DNS root zone, including delegation of individual TLD (.com, .edu , …) management
Q: are there enough 32-bit IP addresses?
ICANN allocated last chunk of IPv4 addresses to RRs in 2011
NAT (next) helps IPv4 address space exhaustion
IPv6 has 128-bit address space

## Slide 76: IP addressing: last words ... 3
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned Names and Numbers http://www.icann.org/
  allocates IP addresses, through 5 regional registries (RRs) (who may then allocate to local registries)
  manages DNS root zone, including delegation of individual TLD (.com, .edu , …) management
Q: are there enough 32-bit IP addresses?
ICANN allocated last chunk of IPv4 addresses to RRs in 2011
NAT (next) helps IPv4 address space exhaustion
IPv6 has 128-bit address space
"Who the hell knew how much address space we needed?" Vint Cerf (reflecting on decision to make IPv4 address 32 bits long)

## Slide 77: NAT: network address translation 1
NAT: all devices in local network share just one IPv4 address as far as outside world is concerned
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
local network (e.g., home network) 10.0.0/24
138.76.29.7
rest of
Internet
datagrams with source or destination in this network have 10.0.0/24 address for source, destination (as usual)
all datagrams leaving local network have same source NAT IP address: 138.76.29.7, but different source port numbers

## Slide 78: NAT: network address translation 2
  all devices in local network have 32-bit addresses in a “private” IP address space (10/8, 172.16/12, 192.168/16 prefixes) that can only be used in local network
  advantages:
    just one IP address needed from provider ISP for all devices
    can change addresses of host in local network without notifying outside world
    can change ISP without changing addresses of devices in local network
    security: devices inside local net not directly addressable, visible by outside world

## Slide 79: NAT: network address translation 3
implementation: NAT router must (transparently):
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
      remote clients/servers will respond using (NAT IP address, new port #) as destination address
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in destination fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 80: NAT: network address translation 4
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1 sends datagram to 128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
10.0.0.1
10.0.0.2
10.0.0.3

## Slide 81: NAT: network address translation 5
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router changes datagram source address from 10.0.0.1, 3345 to 138.76.29.7, 5001,
updates table
10.0.0.1
10.0.0.2
10.0.0.3

## Slide 82: NAT: network address translation6
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives, destination address: 138.76.29.7, 5001
10.0.0.1
10.0.0.2
10.0.0.3

## Slide 83: NAT: network address translation 7
NAT has been controversial:
  routers “should” only process up to layer 3
  address “shortage” should be solved by IPv6
  violates end-to-end argument (port # manipulation by network-layer device)
  NAT traversal: what if client wants to connect to server behind NAT?
but NAT is here to stay:
  extensively used in home and institutional nets, 4G/5G cellular nets

## Slide 84: IPv6: motivation
initial motivation: 32-bit IPv4 address space would be completely allocated
additional motivation:
  speed processing/forwarding: 40-byte fixed length header
  enable different network-layer treatment of “flows”

## Slide 85: IPv6 datagram format
payload (data)
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits
priority: identify priority among datagrams in flow
flow label: identify datagrams in same "flow.” (concept of “flow” not well defined).
128-bit
IPv6 addresses
What’s missing (compared with IPv4):
no checksum (to speed processing at routers)
no fragmentation/reassembly
no options (available as upper-layer, next-header protocol at router)

## Slide 86: Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  no “flag days”
  how will network operate with mixed IPv4 and IPv6 routers?
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers (“packet within a packet”)
  tunneling used extensively in other contexts (4G/5G)

## Slide 87: IPv6: adoption
Google1: ~ 40% of clients access services via IPv6 (2023)
NIST: 1/3 of all US government domains are IPv6 capable

## Slide 88: Middleboxes 1
“any intermediary box performing functions apart from normal, standard functions of an IP router on the data path between a source host and destination host”
Middlebox (RFC 3234)

## Slide 89: Middleboxes everywhere!
enterprise
network
national or global ISP
datacenter
network
NAT: home, cellular, institutional
Firewalls, IDS: corporate, institutional, service providers, ISPs
Load balancers: corporate, service provider, data center, mobile nets
Caches: service provider, mobile, CDNs
Application-specific: service providers, institutional, CDN

## Slide 90: Middleboxes 2
initially: proprietary (closed) hardware solutions
move towards “whitebox” hardware implementing open API
  move away from proprietary hardware solutions
  programmable local actions via match+action
  move towards innovation/differentiation in software
SDN: (logically) centralized control and configuration management often in private/public cloud
network functions virtualization (NFV): programmable services over white box networking, computation, storage

## Slide 91: The IP hourglass
IP
TCP
UDP
HTTP
SMTP
QUIC
DASH
RTP
…
Ethernet
WiFi
Bluetooth
PPP
PDCP
…
copper radio fiber
Internet’s “thin waist”:
one network layer protocol: IP
must be implemented by every (billions) of Internet-connected devices
many protocols in physical, link, transport, and application layers

## Slide 92: The IP hourglass, at middle age
IP
TCP
UDP
HTTP
SMTP
QUIC
DASH
RTP
…
Ethernet
WiFi
Bluetooth
PPP
PDCP
…
copper radio fiber
Internet’s middle age “love handles”?
middleboxes, operating inside the network
NAT
NFV
Firewalls
caching

## Slide 93: Architectural Principles of the Internet
“Many members of the Internet community would argue that there is no architecture, but only a tradition, which was not written down for the first 25 years (or at least not by the IAB). However, in very general terms, the community believes that
RFC 1958
the goal is connectivity, the tool is the Internet Protocol, and the intelligence is end to end rather than hidden in the network.”
Three cornerstone beliefs:
simple connectivity
IP protocol: that narrow waist
intelligence, complexity at network edge

## Slide 94: The end-end argument: 1
some network functionality (e.g., reliable data transfer, congestion) can be implemented in network, or at network edge
end-end implementation of reliable data transfer
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
hop-by-hop (in-network) implementation of reliable data transfer

## Slide 95: The end-end argument: 2
“The function in question can completely and correctly be implemented only with the knowledge and help of the application standing at the end points of the communication system. Therefore, providing that questioned function as a feature of the communication system itself is not possible. (Sometimes an incomplete version of the function provided by the communication system may be useful as a performance enhancement.)
We call this line of reasoning against low-level function implementation the “end-to-end argument.”
Saltzer, Reed, Clark 1981
some network functionality (e.g., reliable data transfer, congestion) can be implemented in network, or at network edge

## Slide 96: Where’s the intelligence?
20th century phone net:
intelligence/computing at network switches
Internet (pre-2005)
intelligence, computing at edge
Internet (post-2005)
programmable network devices
intelligence, computing, massive application-level infrastructure at edge
Notes: The 20th century phone network had dumb network endpoints, really by definition. The end points were rotary phones that maybe only your parents and grandparents remember; they weren’t computers. They really were dumb devices, and therefore the phone network had programmable switches that were quite smart. All functionality – well, all of the intelligence - was implemented within the network. It HAD to be. The end systems could not do anything more than send digits and send audio signals.
When the Internet came along, the endpoints and the switches were both programmable computers. So where to put the complexity? RFC 1958 – the architectural principles of the Internet RFC - that says “intelligence is end to end rather than hidden in the network.” That puts the intelligence clearly at the edge, like we see here. And that’s possible because the edge devices are smart; they’re programmable. Well that’s the diagram as I remember it 20 years ago.
And in the 20 years since, as we see the rise of middleboxes and SDN, we’re now seeing intelligence (in software) layered on top of “dumb” whiteboxes within the network. So I might add a brain here today. And with datacenters and content distribution networks, we see even smarter and more sophisticated application-level infrastructure being connected at points within the network. So now there are clearly much much bigger, much more computationally intensive and complex, endpoints if you will in today’s Internet

## Slide 97: Next Week: The Network Layer: Control Plane
Please read Sections 5.1, 5.3, and 5.4
Computer Networking: A Top-Down Approach . 8th edition Jim Kurose, Keith Ross Pearson, 2020